## Slide 1
rPPG Camera Pipeline
Raw Frame Acquisition & Signal Extraction
Stage 1 of 3 · rppg_pipeline_refined.py
From raw video frames → per-frame RGB blood-volume-pulse signal
BiSeNet
MediaPipe
CHROM
GMM
LBP · SVC
Notes: This is Stage 1 of the rPPG pipeline — the acquisition and signal extraction layer.
It takes raw video as input and produces a clean per-frame RGB time series for downstream heart-rate estimation.
The pipeline combines deep learning (BiSeNet SegFormer), geometric face mesh (MediaPipe 468-point),
classical colour-space rules (YCbCr, Kovac RGB, HSV), Gaussian mixture models, and texture analysis (LBP/SVC).

## Slide 2
What is rPPG?
Remote Photoplethysmography — contactless heart rate from a camera
The Physics
Blood absorbs green light more than oxygenated tissue.
Each heartbeat pushes a bolus of blood through sub-dermal vessels,
creating a ~1–2% oscillation in skin reflectance.
The Challenge
The signal is buried in noise: hair, speculars,
motion, illumination drift, camera AGC.
SNR is typically −20 dB before processing.
The Goal
Extract a clean R/G/B time series from skin pixels only.
Then frequency-estimate to get BPM.
Green-channel reflectance over time
G(t)
t →
~1–2% oscillation
♥ beat
♥ beat
♥ beat
Cardiac band: 0.67–3.5 Hz (40–210 BPM)
Notes: Blood pulsing through sub-dermal vessels changes the amount of green light absorbed by the skin.
This creates a tiny oscillation of about 1-2% in the green channel's reflectance.
The human heart rate spans 40-210 BPM = 0.67 to 3.5 Hz — that is the cardiac band we filter to.
The main challenge: this 1-2% signal is buried under noise from motion, lighting changes, hair pixels, and camera AGC.

## Slide 3
Pipeline Overview
rppg_pipeline_refined.py — end-to-end signal chain
Video Frames
MediaPipe Face Mesh
BiSeNet Skin Parse
Colour Voting ×3
GMM Cluster
Hair Rejection
Final Skin Mask
Prob-Weighted RGB Extraction
CHROM Projection
4× IIR Filter + PCA
OUTPUT → rppg_output.csv (T rows × 26 cols: R/G/B raw + normalised, BVP variants ×5, quality metrics ×8, gt_bpm)
⚡ Caching: BiSeNet every 10 frames · ROI mask only when landmarks move >4px · EMA smooths prob map
⚡ Parallelism: texture maps + colour segmentation run on 2 CPU threads simultaneously (GIL released by numpy/OpenCV)
Notes: Walk through the two-row flow:
Row 1 (left→right): Video frames → MediaPipe gives 468 face landmarks → BiSeNet deep-learning skin classifier runs every 10 frames → three colour-space rules vote on each pixel → GMM clustering confirms skin in Cb-Cr space.
Row 2 (right→left): Texture analysis rejects hair → all evidence combined into final mask → luminance-normalised, probability-weighted R/G/B extraction → CHROM projection → 4 IIR filters plus spatial PCA.
Key performance notes: BiSeNet is the expensive step; caching and thread parallelism keep it under real-time budget.

## Slide 4
Face Detection — MediaPipe FaceLandmarker
468 3D landmarks · VIDEO mode · timestamp-driven Kalman tracker
Why VIDEO mode?
Frames arrive in timestamp order → internal Kalman tracker smooths jitter.
IMAGE mode: each frame independent (slower, no smoothing).
LIVE_STREAM mode: async callbacks — wrong for offline processing.
Landmark → Pixel Coordinate
pts[i] = [lm.x × W, lm.y × H] (normalised → pixel)
pts[33] = outer left eye canthus
pts[263] = outer right eye canthus → mirror detection
pts[10] = superior forehead midline
Confidence thresholds: 0.5 each
detect / presence / tracking
→ num_faces = 1 only
4px movement cache gate
ROI mask only recomputed
when any landmark shifts >4px
Key indices: 33/263 eye outer · 234/454 temple · 70/300 brow outer · 107/336 brow inner · 129/358 nose ala · 172/397 jaw · 54/284 forehead lateral · 10/9 forehead midline
Notes: MediaPipe's FaceLandmarker outputs 468 3D landmarks normalised to [0,1]. We multiply by frame W and H to get pixel coordinates.
VIDEO mode is critical — it keeps the Kalman filter tracker alive across frames. Without it we'd pay the full detection cost every frame.
The camera mirror check: if landmark 33 (left eye outer corner) has smaller x than landmark 263 (right eye outer corner), the camera is NOT mirrored. If reversed, left/right ROI indices are swapped.
The 4-pixel gate prevents wasted polygon recomputation from Kalman filter jitter — sub-4px landmark motion doesn't meaningfully change the ROI shape.

## Slide 5
Deep Learning Skin Segmentation — BiSeNet / SegFormer
jonathandinu/face-parsing · 19-class CelebAMask-HQ · runs every 10 frames
Mix-Trans Stage 1 (1/4)
Mix-Trans Stage 2 (1/8)
Mix-Trans Stage 3 (1/16)
Mix-Trans Stage 4 (1/32)
Lightweight MLP Decoder → logits @ ¼ resolution (1×19×H/4×W/4)
F.interpolate (bilinear, align_corners=False) → full resolution (1×19×H×W)
softmax(dim=1) P(skin) per pixel
argmax == 1 hard skin mask
parse_skin() — what it returns
① Hard mask: bool (H,W) — argmax==1 (skin class)
② Soft prob map: float32 (H,W) — P(skin)∈[0,1]
Hard mask → pixel inclusion/exclusion (Boolean ops)
Soft map → per-pixel weight during RGB extraction
Pixels at 90% confidence contribute 90× more
than pixels at 10% confidence.
Speed: every 10 frames (BISENET_EVERY = 10)
Face crop → rescale to ≤384px max dim → SegFormer
→ resize back to original crop → embed in full frame
EMA (α=0.03) bridges the 10-frame gap smoothly:
sk_prob_smooth += 0.03 × (sk_prob_new − sk_prob_smooth)
Time constant ≈ 1.1 s at 30 fps
torch.no_grad() → disables gradient tracking → 30% faster inference (no backprop graph)
Notes: SegFormer is a mix-transformer encoder with a lightweight MLP decoder. It was fine-tuned on CelebAMask-HQ for 19-class face segmentation. We only use class 1 (skin).
Key innovation: we return BOTH a hard mask AND a soft probability map. The hard mask drives Boolean operations; the soft map drives weighted averaging.
The bilinear upsampling (not nearest-neighbour) produces smooth probability maps — important for the EMA smoothing that follows.
The EMA with alpha=0.03 means the smoothed probability map updates at ~3% of the new frame's probability each frame. At 30fps, this gives a 1.1-second time constant — enough to smooth the 10-frame gaps without introducing significant lag.

## Slide 6
Adaptive Multi-Method Colour Skin Detection
3 independent colour-space methods · per-half fitting · majority vote
Method 1 Adaptive YCbCr
Fit mean±2.5σ on Cb, Cr, Y from BiSeNet seed pixels (per image half) Fallback: Chai & Ngan 1999 Cb∈[77,127] Cr∈[133,173]
Method 2 Kovac RGB Rule
Static structural rule: R>95, G>40, B>20 |max−min|>15 |R−G|>15, R>G, R>B Skin-tone agnostic
Method 3 Adaptive HSV
Circular mean of hue: atan2(mean(sin H), mean(cos H)) Fit ±2.5σ on H and S Wrap-around handled correctly
vote = m1 + m2 + m3 → (vote ≥ 2) | shadow_recovery
Pixel accepted as skin if ≥ 2 of 3 methods agree OR it matches the shadow skin rule
Shadow Recovery Override
Cb∈[60,145] Cr∈[115,190] Y∈[10,45) S≥0.08
Broadened chrominance for dark-lit skin — standard YCbCr fails here.
Image split left/right halves — parameters fitted independently to handle asymmetric lighting (e.g. window on one side of subject) · seed = BiSeNet confirmed pixels ∩ face ROI · min 30 seed pixels required
Notes: Three completely independent methods are used, each operating in a different colour space.
Method 1 (YCbCr): fitted adaptively from BiSeNet-confirmed seed pixels. The mean±2.5σ window adapts to this subject under this lighting. The hardcoded limits are physical constraints — the absolute extremes of valid human skin chrominance from published literature.
Method 2 (Kovac): deterministic, no data-fitting. Works on the physics of how all skin tones interact with broadband light.
Method 3 (HSV): critically uses circular statistics for hue — a plain mean on hue angles near 0°/360° would give completely wrong results.
The left-right split handles asymmetric lighting — if there is a window to the subject's left, the left and right cheeks will have different colour distributions.
Two-of-three majority vote prevents any single noisy method from accepting or rejecting a pixel. The shadow recovery override is an exception — it specifically catches dark skin under shadow that all three methods miss.

## Slide 7
Texture-Based Hair Rejection
LBP · Gradient Coherence · SVC · Specular mask → dual-evidence requirement
LBP Transition Count
8-neighbour binary pattern per pixel → count 0→1/1→0 flips around ring Skin: 0–2 transitions (smooth) Hair: 6–8 transitions (fine texture) Precomputed 256-entry lookup table (module-level, computed once at import)
Gradient Coherence
Sobel → unit direction vectors → smooth with σ=6px Gaussian → magnitude of mean vector Fibre-aligned hair: high coherence Specular/uniform: moderate Random noise: low coherence
Spectral Variation Coeff
SVC = σ/μ in 9×9 local window Var(g) = E[g²] − E[g]² High SVC = locally variable intensity = texture / hair strand pattern Normalised by μ+1 for brightness independence
Specular Mask
pixel > local_mean(31×31) × 1.25 + 25 Mirror-reflected light — physically distinct from skin colour. Specular pixels: IMMUNE to hair rejection (already excluded), not counted in thresholds
Hair pixel ≡ (LBP > p70) AND ((Coherence > p65) OR (SVC > p65)) AND NOT specular
Adaptive percentile thresholds — computed from current ROI distribution, not hardcoded values · Forehead: pct=78 (stricter) · Cheeks: pct=72 (more permissive, sideburns are common)
Dual-evidence requirement: LBP alone is noisy → require corroboration from coherence OR SVC to suppress false positives
All maps computed ONCE per frame → shared by forehead + cheek rejection calls (no recomputation)
Notes: All four texture maps are computed on the illumination-normalised image — the grayscale is divided by a local Gaussian blur, removing slow brightness ramps so LBP sees only fine texture.
LBP transition count: the precomputed 256-entry lookup table converts any 8-bit LBP code to its circular transition count in one array indexing operation — extremely fast.
Gradient coherence: averaging unit vectors (not raw gradients) means the result represents directional alignment, not edge strength. Hair fibres create strong oriented edges aligned in one direction — high coherence.
SVC: coefficient of variation in 9x9 windows — normalised by local mean so dark and bright regions are comparable.
The dual-evidence requirement is the key anti-false-positive design: a noisy skin pixel might have high LBP but low coherence and SVC. Hair will have high LBP AND high coherence OR SVC.

## Slide 8
ROI Polygon Construction
Forehead (18 vertices) · Cheeks (7 vertices each) · Exclusion zones
FOREHEAD (18 vertices)
LEFT CHEEK
RIGHT CHEEK
EXCL ZONE (moustache +beard)
Forehead Polygon
18 vertices tracing: left temple-top → forehead upper arc → midline (pt 10) →
right side → back along brow line → left temple
Deliberate: goes ABOVE the eyebrows to include forehead skin,
excludes brow hair which sits below brow_outer/brow_inner landmarks.
Cheek Polygon — parameterised fractions
ey = eye_out.y + 0.12 × (jaw.y − eye_out.y) ← top edge: 12% down from eye to jaw
ly = eye_out.y + 0.72 × (jaw.y − eye_out.y) ← bottom edge: 72% down
12%: clears the periorbital area (thinner skin, different vasculature)
72%: stops above jaw/chin (beard region)
Medial edge: nose ala x-coordinate · Lateral: temple x-coordinate
Exclusion zones: moustache (pts 129,358,291,61) ∪ beard (pts 61,291,397,152,172) → always removed from final skin mask regardless of colour votes
Notes: The ROI polygons are built from specific MediaPipe landmark indices — not bounding boxes.
Forehead: 18 vertices are enough to trace the hairline boundary faithfully. The polygon deliberately stays above the eyebrow landmarks so brow hair is outside the ROI before even running hair rejection.
Cheeks: the 0.12 and 0.72 fractions are the key parameters. 12% ensures we're below the eye socket — the periorbital area has thinner skin and different photoplethysmography characteristics. 72% ensures we're above the jawline and any beard shadow.
Exclusion zones are a hard rule — moustache and beard skin, even if BiSeNet and all three colour methods say it's skin, is always removed. The haemodynamics of facial hair regions are different from the measurement sites (forehead, cheeks) used to calibrate the CHROM algorithm.

## Slide 9
GMM Clustering in Cb–Cr Space
Gaussian Mixture Model · 3 components · fitted on BiSeNet-confirmed pixels
Cb–Cr Chrominance Space
Cb →
↑ Cr
Component 0 (skin)
Component 1 (shadow skin)
Component 2 (non-skin)
✕ seed μ
fit_gmm() — Algorithm
1. Extract Cb, Cr from BiSeNet-confirmed skin pixels
in the ROI union (forehead ∪ L-cheek ∪ R-cheek)
2. Subsample to ≤4000 points (speed; 4000 is sufficient
for stable GMM convergence)
3. Fit 3-component GMM with full covariance matrices
(allows elliptical, tilted clusters in Cb-Cr space)
4. Identify skin component: closest mean to seed mean
si = argmin ||μk − seed_mean||
5. predict_gmm(): P(component si) > 0.50 → skin
Operates only on ROI pixels (not full frame)
Why 3 components?
Well-lit skin / shadowed skin / transitional skin
A single Gaussian misses multimodal lighting variation.
Y (luminance) is deliberately excluded from GMM — chrominance Cb,Cr is illumination-invariant. GMM with full covariance is strictly more expressive than adaptive rectangular YCbCr thresholds.
Notes: The GMM operates in 2D Cb-Cr space, not the full 3D YCbCr. Luminance is excluded because it depends heavily on lighting — the same skin under bright vs dim light has the same chrominance but very different luminance.
The GMM is fitted on BiSeNet-confirmed skin pixels, which act as an extremely clean seed for the model — we're fitting to known-good skin pixels.
Why 3 components? Under asymmetric lighting, the face shows 2-3 distinct chrominance clusters: well-lit skin, shadowed skin, and a transitional zone. A single Gaussian cannot model this.
The skin component identification after fitting is elegant: instead of labelling components by hand, we find the one whose centroid is closest to the overall seed mean. This is robust regardless of how the EM algorithm orders the components.

## Slide 10
Final Skin Combination & RGB Extraction
Consensus masking · luminance normalisation · probability-weighted mean
Final Skin Combination Logic
comb_sk = BiSeNet | colour_vote | (GMM ∩ vote≥1)
Accept pixel if ANY of:
(a) BiSeNet labels it skin, OR
(b) ≥2 of 3 colour methods agree (majority vote), OR
(c) GMM says skin AND at least 1 colour method agrees
Then SUBTRACT:
· hair_fore (LBP+coherence+SVC on forehead)
· hair_cheek (LBP+coherence+SVC on cheeks)
· excl (moustache ∪ beard exclusion zone)
· specular highlights
fore_skin = comb_sk & fm & ~hair_fore & ~excl & ~spec
l_skin = comb_sk & lcm & ~hair_cheek & ~excl & ~spec
r_skin = comb_sk & rcm & ~hair_cheek & ~excl & ~spec
final = fore_skin | l_skin | r_skin
Luminance-Normalised RGB Extraction
Step 1 — Luminance normalisation
lum = mean(frame[final]) ← mean over skin pixels
fn = frame / lum × 128 ← rescale to fixed reference
Removes camera AGC multiplicative factor.
Any constant works — 128 is mid-scale, intuitive.
Step 2 — Probability-weighted spatial mean
w = sk_prob_smooth[final].clip(0.01)
R_t = Σ(w × fn_R[final]) / Σw
G_t = Σ(w × fn_G[final]) / Σw
B_t = Σ(w × fn_B[final]) / Σw
Why weighted? Pixels at P(skin)=0.90 contribute 90×
more than pixels at 0.01. Downweights boundary pixels
without hard exclusion → no spatial discontinuities.
Per-region: Forehead · L-cheek · R-cheek (min 20px)
Fallback to global value if region too small.
Gate: n_px ≥ 50 skin pixels required before extraction — below this, no signal appended for this frame (face_detected = 0)
9 per-region signals (Rf, Gf, Bf, Rl, Gl, Bl, Rr, Gr, Br) stored for spatial PCA in post-processing
Quality score q = 0.25·BiSeNet_conf + 0.20·vote_mean + 0.20·GMM_agree + 0.15·min(1,coverage/0.40) + 0.12·(1−green_cv/0.15) + 0.08·(1−hair_frac/0.50)
Notes: The combination logic is a union of evidence: any credible source labelling a pixel as skin gets it included — but then geometric and texture filters can veto it.
This is more permissive than intersection-based logic (which would require all methods to agree) and more reliable than union-only (which would include too much noise).
Luminance normalisation is critical for removing camera AGC effects. Without it, a recording where the subject moves into a shadow would show a step change in all three channels — indistinguishable from a very strong physiological event.
The probability-weighted average is the key quality innovation vs simple spatial mean. It continuously penalises uncertain pixels rather than binary-gating them, which produces smoother, more stable time series.
The quality score per frame drives quality-weighted MAE in Stage 2 — frames where the skin detection was confident contribute more to the evaluation.

## Slide 11
CHROM Projection — BVP Signal Extraction
de Haan & Jeanne 2013 · camera-spectral-sensitivity-derived coefficients
CHROM Algorithm — Step by Step
Step 1 — Temporal DC removal
Rn = R / R̄ Gn = G / Ḡ Bn = B / B̄ Divide by temporal mean → each channel becomes dimensionless relative deviation from mean reflectance.
Step 2 — CHROM projection
Xs = 3·Rn − 2·Gn Ys = 1.5·Rn + Gn − 1.5·Bn Coefficients analytically derived from integrals of camera spectral sensitivity over Hb/HbO2 absorption.
Step 3 — Adaptive α cancellation
α = std(Xs) / std(Ys) S = Xs − α·Ys Cancels specular reflection noise common to both Xs and Ys but with different amplitudes.
Step 4 — Linear detrend
S_det = S − polyval(polyfit(t, S, 1), t) Fits a line through S, subtracts it. Removes slow camera gain drift / slow movement.
Spatial Region PCA
9 signals → (3 ROI × 3 channels) stacked matrix X (9×T)
Z-score each row (zero mean, unit variance)
SVD: X = U·Σ·Vᵀ → rows of Vᵀ = principal components
For each of first 3 PCs:
Welch PSD → max in [0.67,3.5Hz] / mean in band
Select PC with highest cardiac-band power ratio
→ Best linear combination across regions & channels
Four IIR Bandpass Filters [0.7–3.5 Hz]
Butterworth order-4
Maximally flat passband (0 ripple)
Chebyshev I order-4 Rp=0.5dB
Equiripple passband, steeper rolloff
Chebyshev II order-4 Rs=40dB
Flat passband, equiripple stopband
Elliptic order-4 Rp=0.5 Rs=40
Equiripple both bands, steepest
All applied with filtfilt → zero-phase (forward+backward pass)
Notes: CHROM is the gold-standard rPPG BVP extraction algorithm from de Haan & Jeanne 2013.
The three projection coefficients (3,-2 for Xs and 1.5,1,-1.5 for Ys) are NOT empirical — they are analytically derived from integrating the camera's spectral sensitivity curves over the haemoglobin absorption spectrum. They are physically grounded.
The alpha parameter is adaptive per recording: it adjusts the relative scaling of Xs and Ys to cancel specular reflection. Specular reflection adds a component proportional to the illumination spectrum to both Xs and Ys — alpha removes it.
Spatial PCA is a generalisation of CHROM: instead of manually defining the projection direction, SVD finds the linear combination of all 9 regional signals that maximises variance in the cardiac band. It automatically discovers the best weighting of forehead vs cheeks vs L vs R vs R/G/B.
All four IIR filters are applied with filtfilt — this doubles the effective order but removes all phase distortion. Phase distortion would shift different frequency components in time, distorting the BVP waveform shape.

## Slide 12
Output CSV & Per-Frame Quality Metrics
T rows × 26 columns · 8 quality metrics · composite quality score
Timing
frame_index
time_s
Raw RGB
R/G/B_skin_raw
R/G/B_normalized
Frame stats
frame_luminance
face_detected
skin_pixel_count
BVP variants ×5
BVP_detrended
BVP_butterworth
BVP_cheby1
BVP_cheby2
BVP_elliptic
BVP_pca
Ground truth
gt_bpm
Quality ×8
bisenet_conf
vote_mean
highconf_pct
roi_coverage
green_cv
hair_rej_frac
clust_agree
quality_score
Quality Metrics Explained
bisenet_conf
Mean BiSeNet P(skin) over accepted pixels · 0–1
vote_mean
Mean 3-method colour agreement / 3 · 1.0 = unanimous
highconf_pct
Fraction of skin pixels where ALL 3 colour methods agreed
roi_coverage
skin_px / anatomical_ROI_area · fraction of face covered
green_cv
std(G) / mean(G) over skin pixels · low = spatially uniform
hair_rej_frac
hair_pixels / ROI_area · high = mostly hair, low quality
clust_agree
Fraction of skin pixels also in GMM skin cluster
quality_score
0.25·bc + 0.20·vm + 0.20·ca + 0.15·cov + 0.12·(1−gcv) + 0.08·(1−hrf)
Notes: The output CSV is the contract between Stage 1 and Stage 2. Every row is one successfully processed frame.
The 5 BVP variant columns let Stage 2 directly compare filter families without re-running the acquisition pipeline.
The 8 quality metrics per frame are the key innovation for downstream quality-gating. Stage 2 uses quality_score to weight-average the BPM error — frames where the skin detection was poor contribute less to the reported accuracy.
The composite quality score weights BiSeNet confidence highest (25%) because the deep learning classifier is the most reliable single predictor of skin detection quality. Colour voting (20%) and GMM agreement (20%) are independent corroborating evidence. ROI coverage, green CV, and hair fraction are secondary factors.

## Slide 13
Key Design Decisions
The three principles that drive the entire acquisition pipeline
1
1. Compute Once, Reuse Everywhere
compute_frame_maps() runs once per frame → dict of all colour representations compute_texture_maps() runs once → shared by forehead + cheek hair rejection No function re-converts any colour space. Eliminates redundant cvtColor() calls. Result: ~3× speedup vs naïve implementation at no code complexity cost.
2
2. Cache Aggressively, Invalidate by Condition
BiSeNet → every 10 frames (skin changes at ≤1Hz; 3Hz refresh is sufficient) ROI masks → only when landmarks shift >4px (sub-4px = tracker noise, not real motion) GMM fit → same cadence as BiSeNet (refit on fresh seed pixels) EMA α=0.03 → bridges 10-frame gap, τ≈1.1s, no discrete jumps in weighted means Result: neural network cost reduced from 100% to ~10% of frames.
3
3. Require Consensus, Not Unanimity
A pixel is accepted as skin if ≥2 of 3 colour methods agree, OR BiSeNet, OR GMM+1 Then VETOED by hair texture, exclusion geometry, specular detection Permissive inclusion → tight exclusion is more robust than either alone. BiSeNet alone fails on beard shadow. YCbCr alone fails in unusual lighting. LBP alone generates false hair flags. Each method's weaknesses cancel out.
Notes: These three decisions explain WHY the code is structured the way it is.
Decision 1 (compute once): compute_frame_maps() is called at the top of the per-frame loop and passed as a dict. Every subsequent function (adaptive_color_skin, compute_texture_maps, final combination) reads from this dict. This is not just an optimisation — it also ensures consistency: all methods see exactly the same floating-point representation of each channel.
Decision 2 (caching): the EMA is subtle but important. Without it, every 10th frame would have a discrete jump in the probability-weighted RGB means when BiSeNet produces a new estimate. The EMA smooths this to a ~1-second ramp, which is invisible in the BVP signal at cardiac frequencies.
Decision 3 (consensus): this is the most important architectural decision. No single method is trusted. The ensemble approach was tested against simpler designs (BiSeNet alone, YCbCr alone) and always outperforms in terms of quality_score and downstream BPM accuracy.